## Slide 1: 지진원 특성평가 Characterization of Seismic Sources - Part II -
Supreme Course I

## Slide 2: Chapter 5 Earthquake Catalog

## Slide 3
Origin Parameters
  (Origin) Time
    Time of earthquake occurrence
    usually corresponds to the rupture initiation time
  Location
    Locus at which an earthquake occurred, hypocenter
      Usually corresponds to the rupture initiation point
    Also described by epicenter and depth
    Epicenter
      Vertical projection of hypocenter to the surface
      Described in geographical latitude & longitude
    Focal depth
      Depth (km) to the hypocenter
    Distances to an earthquake
      Hypocentral distance (), epicentral distance (), focal depth ()
      ; not a propagation distance
Preparation of Catalog

## Slide 4
Origin Parameters (continued)
  Size
    Various magnitude scales being used
    Body-wave magnitude
      Sensitive to high-frequency content → larger value for deeper event
      Saturated for large earthquakes
    Surface-wave magnitude
      Measure of longer period energy → smaller value for smaller event
    Moment magnitude
      Measure zero-frequency energy
      No saturation
      Physics-based value
      Representative measure of size
        : seismic moment in dyne-cm
      Bridge connecting to geology

## Slide 5
Integration of Catalogs
  To expand earthquake data by combining various catalogs covering different periods, different regions (ergodic assumption)
  General requirements
    Description by unified quantities
    Accuracy assessment
  Important properties to be checked
    Unification of description
      origin times
        Use of UTC (Coordinated Universal Time) or a single local time
      Unification of magnitude scale
        Use of a single magnitude scale: moment magnitude is preferred
    Accuracy checks
      Error range of magnitude
      Error range of location

## Slide 6
Background
  The very 1st step of any analysis using earthquake catalog is to assess the completeness of the catalog at hand
    =0.78, 1.11, 1.17 for =1.9, 3.0, 3.3 [노명현 외(2000)]
Completeness Assessment of Catalog

## Slide 7
Categories of Assessment Methods
  Network-based methods
    Use detection capability of a seismic network
      Background noise, network configuration, instrumentation, etc.
  Catalog-based methods
    Use day-to-night noise modulation
      Proposed by Rydelek and Sacks (1989)
      Can be considered as a network-based method
    Assumption of self-similarity for earthquake frequencies
      Focus of this course
General Procedure
  Introducing the cut-off magnitude,
    Starting from minimum magnitude of catalog
    Gradually increasing by magnitude interval width
  Repetition of analysis for increasing
  if certain conditions are met

## Slide 8
General Procedure (continued)
  Repetition of the above procedure to estimate for bootstrap replicas of the catalog
  Calculation of the location and scale of for the replicas
Definitions of
  Minimum magnitude above which all earthquakes were completely reported (Rydelek and Sacks, 2000)
  Minimum magnitude that preserves the information on seismicity parameters, i.e., , Richter-b (Noh, 2019)

## Slide 9
Maximum Curvature Method
  Wiemer and Wyss (2000)
  is located at the maximum of the non-cumulative frequency
  Simplest method, underestimation of by 0.2

## Slide 10
Goodness-of-Fit Test
  Wiemer and Wyss (2000)
  where

## Slide 11
b-Value Stability Test
  Firstly proposed by Cao and Gao (2002)
  Later modified by Woessner and Wiemer (2005)
      : estimate of -value for magnitude
    ← =5, is quite sensitive to
    (Shi & Bolt, 1982)

## Slide 12
Entire-Magnitude-Range Method
  Firstly proposed by Ogata and Katsura (1993)
  Later modified by Woessner and Wiemer (2005)
    Maximum likelihood estimation of parameters
      Modelling incomplete portion at smaller magnitudes by the error function
      Modelling complete portion by exponential magnitude distribution
    to maximize sum of likelihoods for the two portions

## Slide 13
Change-Point Detection Method
  Amorese (2007)
  Detecting multiple change-points in b-estimates
  to minimized the Type I error

## Slide 14
Chi-Square Test
  Noh (2019)
  Pearson’s test statistic:
    : number of observed events with
    : number of predicted events with
      and
      Three constraints
  : 1st cross-over magnitude

## Slide 15: Chapter 6 Characterization of Seismic Sources - Catalog Based -

## Slide 16: Introduction
Major Seismicity Parameters
  Maximum magnitude, Richter-b, annual occurrence rate
Seismic vs. Geologic Approaches
  Seismicity-Based Approaches (Probabilistic)
    Open the only option in regions with limited seismic record and limited geological investigations
    Particularly useful for constraining rates of small to moderate events that do not provide surface evidence
  Geological Approaches (Deterministic)
    Works well in active areas with a significant history of earthquake occurrence and geological investigations
    Particularly useful for constraining rates of the largest events with surface evidences
  Cross Check
    If two approaches are available, their estimates can be used for the cross check

## Slide 17
Inadequacy of LSM
  Common Assumptions
    Almost always
      Independency of samples (i.e., observed data)
    In most cases
      Independent, identically distributed (i.i.d. assumption)
  Least-Squares Method (MSM)
    Log-linear fitting of G-R relation
      , where is the number of events
    Violation of independency assumption
      A change of the frequency at a magnitude affects all frequencies at magnitudes less than that magnitude
    Larger events are repeatedly counted in the smaller event counts
      Lower b-values (Bender, 1983)

## Slide 18: Magnitude Distribution
Exponential Model
  Gutenberg-Richter Relation
    →
    For ,
      , , and
  Derivation of PDF for
    Normalization:
    PDF:
    CDF:

## Slide 19
Exponential Model (continued)
  Introducing the magnitude upper bound
    or
    PDF:
    CDF:

## Slide 20
Characteristic Earthquake Model
  Schwartz and Coppersmith (1984)
    ,
    ←

## Slide 21
Characteristic Earthquake Model (continued)
  PDF:
  where and
  Task: Derive the following formula

## Slide 22: Estimation of Richter-b
Maximum likelihood method (MLM)
  Probability density function of magnitude
    where ,
    The parameter has disappeared due to normalization of a PDF!
      Annual rate cannot be estimated from magnitude PDF only
  Likelihood function
    , or
    , where
  Maximum likelihood estimate: and
    For ;
      (Aki, 1965); (Utsu, 1965) by the method of moments
      for magnitude grouping with (Utsu, 1966)

## Slide 23
Maximum likelihood method (MLM)
  Maximum likelihood estimate (continued)
    For finite
      (Page, 1968)
      for magnitude grouping with (Karnik, 1971)
      for magnitude grouping with & unequal observation period, (Weichert, 1980), using

## Slide 24
    Extension to incomplete catalogs (Kijko & Smit, 2012)
      where and

## Slide 25: Estimation of Annual Rate
Basic Approach
  For events during years
    if is the annual rate of events in -th year
  For the Poisson process with mean annual rate,
  Likelihood function
    , or
  ML Solution
    , or

## Slide 26
Refined Formulation
  Exponential distribution with
  Mean frequency of events of magnitude
  For such a small that no more than one event in any magnitude interval
    , , or
  Likelihood function, as ()
    , or

## Slide 27
Refined Formulation (continued)
  ML Solution
    Estimation of and is completely separated!
  Tasks
    Calculate variance of the above estimate of .
    [Hint] Use .
    Extend estimate of for a finite .
    [Hint] Replace by , where and the upper integration limit by .

## Slide 28
Magnitude-Grouped, Unequal Observation Time
  Noh (unpublished)
  Probability over -th magnitude interval
    ↔ (Weichert, 1980)
  Mean frequency of events of -th magnitude interval
  Poisson probability for frequency
  Log-likelihood function

## Slide 29
  Log-likelihood function (continued)
    where , , , and
  Estimation of
    (1)
    (2)
      Estimation of and is not separated!

## Slide 30
  Estimation of
    (3)
    (4)
    where

## Slide 31: Estimation of
Introduction
  Why no maximum likelihood estimates using ?
    ,
    where
  General form of estimator
    Usually, includes
      (Kijko, 2004)
    (inner) Iteration scheme is required
      : uncertainty related to the determination of
      : uncertainty related to the magnitude determination ()

## Slide 32
  List of Methods
Class | Name | Remark
Parametric | T-P | Procedure by Pisarenko et al. (1996)
 | K-S | Procedure by Kijko & Sellevoll (1989)
 | T-P-B | Tate-Pisarenko-Bayes procedure
 | K-S-B | Kijko-Sellevoll-Bayes procedure
Non-parametric | N-P-G | Non-parametric procedure with Gaussian kernel
 | N-P-OS | Non-parametric procedure based on order statistics
 | R-W | Robson-Whitlock procedure
 | R-W-C | Robson-Whitlock-Cooke procedure
 | F-L-E | Procedure based on a few large earthquakes
Fit of CDF | L1-Fit | Procedure based on fit of L1 norm CDF
 | L2-Fit | Procedure based on fit of L2 norm CDF

## Slide 33
Parametric Approaches
  Tate-Pisarenko Procedure
    Order statistics of earthquake magnitude:
      is independent, identically distributed by
    For transformation
      is a uniform deviate such that
      and
    CDF of the largest among , that is is
    PDF of is

## Slide 34
  Tate-Pisarenko Procedure (continued)
    Expectation
    Best unbiased estimation of is
    Using the Taylor expansion of at
      (1)
    Taking average of both sides of (3) and using
    We arrive at

## Slide 35
  Tate-Pisarenko Procedure (continued)
    For a large
    Finally
      (2)
    For doubly truncated PDF,
    The estimator is,
  Notes
    (2) was probably first derived by Tate (1959)
    It was used by Pisarenko et al. (1996)

## Slide 36
  Kijko-Sellevoll Procedure
    Kijko & Sellevoll (1989)
    From order statistics, CDF of the largest observed magnitude among events, is
      or
      or
    For large , (Cramér, 1961)
    For doubly truncated PDF,
        , , and
        ; exponential integration function

## Slide 37
  Kijko-Sellevoll Procedure (continued)
    The estimator is,
    While the exact formula of is reported, it is not discussed here because it does not gives an improved accuracy but is just complicated.
    A direct numerical integration, such as the Romberg integration, of yields an accurate enough result.

## Slide 38
  Tate-Pisarenko-Bayes Procedure
    Assuming a gamma distribution for , Campbell (1982) showed
        , ,
        is a known value of and a known standard deviation of , of which values are taken from the their estimates to be discussed in the subsequent section
    For doubly truncated PDF,
    T-P-B yields estimate of very close to that of T-P

## Slide 39
  Kijko-Sellevoll-Bayes Procedure
    Assuming a gamma distribution for , Campbell (1982)
    Using Cramér’s approximation
      ,
        where ,
    K-S-B yields estimate of very close to that of K-S

## Slide 40
Non-Parametric Approaches
  Non-Parametric with Gaussian Kernel Procedure
    Kernel estimator of actual, unknown PDF
        : positive smoothing factor
        : kernel function, a PDF, symmetric about zero
      Estimation is not sensitive to the kernel function
        Choice is the standard normal PDF, normalized in the range
        But the choice of a smoothing factor is crucial
        : standard normal CDF

## Slide 41
  Non-Parametric with Gaussian Kernel Procedure (continued)
    Estimators
      T-P procedure:
      K-S procedure:

## Slide 42
  Non-Parametric Procedure Based on Order Statistics
    For ordered observations,
      (Cooke, 1979)
    Approximate of integral
      For large ,
    Estimator of

## Slide 43
  Robson-Whitlock Procedure
    For ordered observations, , Robson and Whitlock (1964) proposed
    For a doubly-truncated exponential distribution
      ,
    While its simplicity makes it very attractive, it is known that reduction of bias is achieved at the expense of mean squared error.

## Slide 44
  Robson-Whitlock-Cooke Procedure
    Cooke (1979) showed that reduction of the mean squared error of the R-W estimator is possible when some information, about the shape of the upper tail of PDF,
    For a doubly-truncated exponential distribution,
      ,

## Slide 45
  Procedure Based on a Few Largest Earthquakes
    Gnedenko (1943) suggested for a very broad class of
      When is near to the upper end point
      is linear in
        : coefficients to be determined,
        : order statistics
        : the number of largest earthquakes
    For truncated distributions, the mean squared error of is minimized when
      , and
      That is,
      Due to Quenouille (1965), an improved is

## Slide 46
  Procedure Based on a Few Largest Earthquakes (continued)
    The estimators for
      ,
      ,
    Note that
      When we have sufficient sample, ,
      Therefore, this estimator is useful only when we have limited information, a few large earthquakes

## Slide 47: Fit of CDF Approach
Fit of CDF Approaches
  Procedure Based on L1-Norm of CDF
    For ordered observations, , the set of model parameters can be found by minimizing the misfit function
      ,
    In case of the doubly-truncated exponential PDF,
    can be calculated by numerical methods, such as simplex method (Press et al, 1994)
    Note that, the misfit function of norm could have multiple extrema for more than one parameter

## Slide 48
  Procedure Based on L2-Norm of CDF
    For ordered observations, , the set of model parameters can be found by minimizing the misfit function
      ,
    Solving this the least-squares method is equivalent to the maximum likelihood method with the assumption that the distribution of the CDF residuals is of Gaussian

## Slide 49
Variance of for the Gaussian Procedure
  Generalized misfit function to be minimized
    ,
      : -th observation
      : model prediction for -th observation
      : prediction error or noise at -th observation
  For the generalized Gaussian process
      : location parameter (, assuming has a zero mean)
      : scale parameter
  The covariance matrix is
    , where ;

## Slide 50
Variance of for the Gaussian Procedure (continued)
  Ordinary Gaussian process;
  Norm:
    ;
  Norm:

## Slide 51
Variance of for the Gaussian Procedure (continued)
  Finally, the matrix is calculated as follows
    ;
  Therefore,
    ; where or

## Slide 52
Alternative Approach to Estimate Variances
  Method in the previous slides is quite general, but somewhat complicated
  Considering the sensitivity of to , it would be better to separately estimate by a proper method, if exists.
  We do have such a method, Weichert (1980) discussed in the section ‘Estimation of Richter-b’
  Moreover, use of Weichert (1980) is consistent with the other estimators introduced in this course
  In the following, we use by Weichert so that there is only one parameter to be estimated,
  As before, the cost or misfit function is
    and
      and

## Slide 53
Alternative Approach to Estimate Variances (continued)
  Norm:
    Minimization of cost (misfit) function
      or
      Can be solved by a root-finding algorithm
    , where

## Slide 54
Alternative Approach to Estimate Variances (continued)
  Norm:
    Minimization of cost (misfit) function
      or
      Can be solved by a root-finding algorithm
    , where

## Slide 55
On the Use of the CDF-Fitting Procedure
  These methods assumes that the CDF, is known
  If so, in spite of efforts up to now, there is no reason to stick to this procedure
  Instead, we can use the parametric procedures

## Slide 56: Iterative Scheme for of &
Inter-Linkage of b & Mmax
  In parametric models, they are linked each other
    Estimation of b
    Estimation of
  To estimate one, the information of the other is necessary

## Slide 57
Simultaneous Estimation
  Iterative scheme by Noh (2014)
    Step 1: estimate first with observed
    Step 2: estimate using estimated in Step 1
    Step 3: re-estimate using estimated in Step 2
    Step 4: re-estimate using estimated in Step 3
    Step 5: repeat Steps 3 and 4 until certain exit conditions are met

## Slide 58
  Performance of Iterative Scheme (Noh, 2014)

## Slide 59
  Recommendations (Noh, 2014)
    Estimate first,
      can effectively replace the unknown
    Then estimate
    Ex: Weichert (1980) used in place of
  Better Estimate by Iterative scheme
    Starting with estimation first with for

## Slide 60: Chapter 7 Use of Geologic and Geodetic Information

## Slide 61: Estimation of Annual Rates
Bridge between Geologic and Seismic Information
  Seismic moment: (Aki, 1966)
    : rigidity, ~3x1011 dyne/cm2
    : rupture area on a fault plane undergoing slip during an earthquake
    : average displacement over the rupture area, i.e.,
      , where is a displacement at a rupture point.
  If little seismic information
    can be used to estimate the amount of seismic moment release
  If geologic and seismic information available
    Estimates are confirmed through comparison

## Slide 62
Extension to Whole Fault Surface
  Seismic moment rate (Brune, 1968)
    Total average slip:
    Total moment rate:
      : total moment rate during a period
      : average slip rate over the whole fault plane
Moment Magnitude
    =1.5 & =16.05 (Hanks and Kanamori, 1979)

## Slide 63
Slip Rate Constraint
  Exponential Distribution
    Gutenberg-Richter relation (Richter, 1958)
      or
        : the number of earthquakes greater than
    Earthquake occurrence density for total events in [,)
    Earthquake occurrence density for total events in [,]
      Normalization:
      (7-1)

## Slide 64
Slip Rate Constraint
  Exponential Distribution (continued)
    Cumulative number of earthquakes in [,]
      e.g., Youngs & Coppersmith (1985)
    Total moment rate during a period
      , or (7-2)
      , or
      where and (Youngs & Coppersmith, 1985)

## Slide 65
It is worth noting:
  From (7-1), can be expressed by PDF:
  But should not be interpreted by a PDF because the integration in (7-2) extends to , below
    here is just a function that has the same functional form as the PDF
  Nevertheless, the analogy to a PDF is quite useful when only the PDF is defined
  Example: Delta distribution:
    /
  Conversely, we can find from the formula of

## Slide 66
Characteristic Earthquake Model
  Schwartz and Coppersmith (1985)
  Let (7-3)
    : the number of event in
    : the number of event in
  From the right figure, we see that
    (dropping the dot-hat)
  Using (7-1) and
    (7-4)

## Slide 67
Characteristic Earthquake Model (continued)
  Since
  Inserting into (7-4)
      where

## Slide 68
Characteristic Earthquake Model (continued)
  Substituting by
      where and
  As a by-product, we obtained the PDF
  Total moment rate
    , or

## Slide 69
Displacement Distribution on Fault Plane
  Normalized slip: ) (Biasi et al., 2013)
    : slip normalized by average slip over the whole fault length
    : normalized fault length,

## Slide 70: Estimation of
Assumption
  Growth of the fault dimension due to the occurrence of earthquakes is negligible to small
Use of Geologic and Geodetic Data
  is observed when the whole fault surface is ruptured
  Empirical relations on the magnitude-rupture length or magnitude-rupture area can be used for the estimation of

## Slide 71: Chapter 8 Topical Issues

## Slide 72: Effect of Catalog Combination
Purpose
  To increase catalog size for stable estimation of seismicity parameter by extending spatial and/or temporal domains
Case study (Noh, 2020)
  3,255 events of M0.1~M5.2 from KMA catalogs for
    Period: 1981~2015
    Events designated as ‘domestic’ by KMA
  Sub-catalogs
    Sub-catalog SL includes the events occurred in the land of South Korea
    Sub-catalog NL includes the events occurred in the land of north Korea
    Sub-catalog AO includes the off-shore events

## Slide 73
  Estimates of
    Estimates of are high even for the SL, considering the Korean seismic network density
    for the AO and the NL are lager than that for the inland events SL
    for the sub-catalogs (SL+AO) or (SL+AO+NL) is much higher than those for the sub-catalog SL as well as the sub-catalog AO or the sub-catalog NL

## Slide 74
  There exits a trade-off between the completeness and the spatiotemporal coverage of an earthquake catalog
    To enhance the completeness of an earthquake catalog, divide the catalog into sub-catalogs considering the spatiotemporal detectability of the seismic network
    Or, one may combine several catalogs to cover a larger region or a longer period at the expense of catalog completeness

## Slide 75: Earthquake Double Counting
Types of Seismic Sources
  Fault source
    A fault capable of generating earthquakes
  Area (Volume) source
    A zone where earthquake occurs but the faults responsible those earthquakes are not identified
    Could be a large background source, or further divided into several area sources depending on the difference in seismic activities
Spatial Overlapping
  A fault source generally passes through one or more area sources
  Those earthquakes counted in for a fault source should not be counted in for the area sources again that contain the fault source
    If a new fault source added, the seismicity of all surrounding area sources should be re-assessed

## Slide 76
Practical Limits
  Important seismic parameters to be re-assessed
    Annual rate, Richter-b,
  Difficulty in separation of earthquakes
    Complete separation of earthquakes of a fault source from the surrounding area sources is impossible due to the uncertainties of the earthquake location and the subsurface structure of fault
    Especially, the earthquake location is more uncertain for smaller and older earthquakes
    There are some cases where all the large earthquakes, say, larger than M=6.5 are attributed to fault sources
  Difficulty in the Quaternary faults in Korea
    They have been identified solely based on surface geological investigation
    There are big uncertainties in the seismic parameter assessed from the geological observation only

## Slide 77
Valid Principles
  Axiomatic proposition
    There has been a fault. Therefore, finding out the fault does not change the past earthquake history.
    (1)
      where and are the number of sources and annual rate of the -th source before a new fault source is added, and
      and are the number of sources and annual rate of the -th source after a new fault source is added
  Limit of the axiomatic proposition
    It does not separate earthquakes themselves, but just annul rates
    Thus, it offers no information necessary for re-assessment of the Richter-b and
  Re-assessment of area sources
    Annual rates
      Fault: annual rate can be estimated from the geodetic information or paleo-seismic survey
      Area: annul rates of surrounding area sources can be corrected to the remaining amount of annual rate

## Slide 78
Valid Principles
  Re-assessment of area sources (continued)
      Fault: can be estimated from the geologic information
      Area: of an area source is estimated from the earthquake catalog
        Since the estimate is sensitive to the large observed earthquakes, re-assessment of of an area source is of particular importance after some large earthquake are assigned to a fault source
        Re-assessment of is possible only when earthquakes themselves were separated
    Richter-b
      As long as earthquakes themselves are not separated, the re-assessment of the Richter-b is not possible
      Fortunately, the Richter-b varies little among seismic sources and the separation of earthquakes do not always results in the change of the Richter-b
      It is not so dangerous to use the Richter-b of nearby sources
      This procedure is valid for a fault source as well as an area source

## Slide 79
Example Calculation of PSHA (Noh, 2023)
  Source map & sites
  GMM: Sadigh et al. (1997), no variability
  Spectral frequencies: PGA @ 100 Hz
  GM levels: 10 values at
    50, 100, 150, 200, 250, 300, 350,
    400, 450, 500 gals
  Magnitude-Rupture relation
    For length (km):
  Truncated exponential mag. distribution
  Uniform distribution for focal depths
  Aspect ratio: 2

## Slide 80
Site A
Site B

## Slide 81: References
    노명현, 2023. 지진의 이중산입에 대한 소고, 한국지진공학회 논문집, 27, 157-162.
    노명현, 이상국, 최강룡, 2000. 지진활동 매개변수 추정을 위한 기상청 지진목록의 최소규모 분석, 지구물리와 물리탐사, 3, 261-268.
    Aki, K., 1965. Maximum likelihood estimate of b in the formula and its confidence limits, Bull. Earthquake Res. Inst., Tokyo University, 43, 237-239.
    Aki, K., 1966. Generation and propagation of G-waves from the Niigata earthquake of June 19, 1964. 2. Estimation of earthquake movement, released energy, and stress-strain drop from G-wave spectrum, Bull. Earthquake Res. Inst., Tokyo Univ. 44, 23-88.
    Amorese, D., 2007. Applying a change-point detection method on frequency-magnitude distributions, Bull. Seism. Soc. Am., 97, 1742-1749.
    Bender, B., 1983. Maximum likelihood estimation of b values for magnitude grouped data, Bull. Seism. Soc. Am., 73, 831-851.
    Berrill, J.B. and R.D. Davis, 1980. Maximum entropy and the magnitude distribution, Bull. Seism. Soc. Am., 70, 1823-1831.
    Biasi, G.P., Weldnon, R.J.I., and Dawson, T.E., 2013. Appendix F: Distribution of Slip in Ruptures. Open File Report 2013-1165. USGS.

## Slide 82
    Brune, J.N., 1968. Seismic moment, seismicity and rate of slip along major fault zones, J. Geophys. Res. 73, 777-784.
    Campbell, K.W., 1982. Bayesian analysis of extreme earthquake occurrences. Part I. Probabilistic hazard model, Bull. Seism. Soc. Am., 72, 1869-1705.
    Cao, A.M. and S.S. Gao, 2002. Temporal variation of seismic b-values beneath northeastern Japan island arc, Geophys. Res. Lett., 29, doi 10.1029/2001GL013775.
    Cooke, P. (1979), Statistical inference for bounds of random variables, Biometrika, 66, 2, 367-374, DOI: 10.1093/biomet/66.2.367.
    Cornell, C.A., 1972. Bayesian statistical decision theory and reliability-based design, Proceedings of the International Conference on Structural Safety and Reliability, April 9-11, 1969, Washington, D.C., Smithsonian Institute, 47-66.
    Cornell, C.A. and E.H. Van Marke, 1969. The major influences on seismic risk, Proceedings Third World Conference on Earthquake Engineering, Santiago, Chile, A-1, 69-93.
    Cramér, H., 1961. Mathematical Methods of Statistics, 2nd ed., Princeton University Press, Princeton.
    Gnedenko, B. (1943), Sur la distribution limite du terme maximum d’une série aléatoire, Ann. Math. 44, 3, 423-453 (in French).
    Hanks, T.C. and H. Kanamori, 1979. A moment magnitude scale, J. Geophys. Res., 84, 2348-2350.

## Slide 83
    Johnston, A.C., Coppersmith, K.J., Kanter, L.R., and Cornell, C.A., 1994. The earthquakes of stable continental regions: final report submitted to Electric Power Research Institute: TR-102261.
    Karnik, V.K., 1971. Seismicity of the European area, Part 2. Academia, Publishing House of the Czechoslovak Academy of Sciences, Praha, Czechoslovakia, 123-169.
    Kijko, A., 2004. Estimation of the maximum earthquake magnitude, . Pure and Applied Geophysics, 161, 1-27.
    Kijko, A., and M.A. Sellevoll (1989), Estimation of earthquake hazard parameters from incomplete data files. Part I. Utilization of extreme and complete catalogs with different threshold magnitudes, Bull. Seism. Soc. Am. 79, 3, 645-654.
    Kijko, A. and A. Smit, 2012. Extension of the Aki-Utsu b-value for incomplete catalogs, Bull. Seism. Soc. Am., 102, 1283-1287.
    Noh, M., 2014. A parametric estimation of Richter-b and from an earthquake catalog, Geosciences Jour., 18, 339-345.
    Noh, M., 2016. On the Poisson process of the Korean earthquakes, Geosciences Jour., 20, 775-779.
    Noh, M., 2019. Assessment of the completeness of earthquake catalogs, Geosciences Jour., 23, 253-263.

## Slide 84
    Noh, M., 2020. Effect of combining catalogs with different completeness: EGU2020-1749, EGU General Assembly 2020, Vienna.
    Ogata, Y. and K. Katsura, 1993. Analysis of temporal and spatial heterogeneity of magnitude frequency distribution inferred from earthquake catalogs, Geophys. J. Int., 113, 727-738.
    Page, R., 1968. Aftershocks and microaftershocks of the great Alaska earthquake of 1964, Bull. Seism. Soc. Am., 58, 1131-1168.
    Pisarenko, V.F., Lyubushin, A.A., Lysenko, V.B., and Golubieav, T.V., 1996. Statistical estimation of seismic hazard parameters: maximum possible magnitude and related parameters, Bull. Seism. Soc. Am., 86, 691-700.
    Press, W.H., B.P. Flannery, S.A. Teukolsky, and W.T. Vetterling (1994) Numerical Recipes: The Art of Scientific Programming, Cambridge University Press, New York.
    Quenouille, M.H. (1956), Notes on bias in estimation, Biometrika, 43, 3-4, 353-360, DOI: 10.1093/biomet/43.3-4.353.
    Richter, C.F., 1975. Elementary Seismology, W.H. Freeman and Company, San Francisco, California.
    Robson, D.S., and J.H. Whitlock (1964), Estimation of a truncation point, Biometrika, 51, 1-2, 33-39, DOI: 10.1093/biomet/51.1-2.33.
    Rydelek, P.A. and Sacks, I.S., 1989. Testing the completeness of earthquake catalogs and the hypothesis of self-similarity, Nature, 337, 251-253.

## Slide 85
    Sadigh, K., Chang C.-Y., Egan J.A., Makdisi F., and Youngs R.R., 1997. Attenuation relationships for shallow crustal earthquakes based on California Strong Motion Data, Bull. Seism. Soc. Am., 68, 180-189.
    Schwartz D.P. and Coppersmith, K.J., 1984. Fault behavior and characteristic earthquakes: examples from the Wasatch and San Andreas faults, J. Geophys. Res., 89, 5681-5698.
    Tate, R.F., 1959. Unbiased Estimation: Function of Location and Scale Parameters, Ann. Math. Statist., 30, 331–366.
    Utsu, T., 1965. A method for determining the value of b in formula showing the magnitude-frequency relation for earthquakes, Geophys. Bull. Hokkaido University, 13, 99-103.
    Utsu, T., 1966. A statistical significance test of the difference in b-value between two earthquake groups, J. Phys. Earth, 14, 37-40.
    Weichert, D.H., 1980. Estimation of the earthquake recurrence parameters for unequal observation periods for different magnitudes, Bull. Seism. Soc. Am., 70, 1337-1346.
    Wiemer, S. and M. Wyss, 2000. Minimum magnitude of complete reporting in earthquake catalogs: examples from Alaska, the Wester United States, and Japan, Bull. Seism. Soc. Am., 84, 974-1002

## Slide 86
    Wells, D.H. and Coppersmith, K.J., 1994. New empirical relationships among magnitude, rupture length, rupture width, rupture area, and surface displacement, Bull. Seism. Soc., Am., 84, 974-1002.
    Woessmer, J. and S. Wiemer, 2005. Assessing the quality of earthquake catalogues: estimating the magnitude of completeness and its uncertainty, Bull. Seism. Soc. Am., 95, 684-698.
    Youngs, R.R. and Coppersmith, K.J., 1985. Implications of fault slip rates and earthquake recurrence models to probabilistic seismic hazard estimates, Bull. Seism. Soc. Am., 75(4), 939-964.